## Slide 1
Accelerated Explicit Dynamics Simulations of Impact Problems Using GPU-Enabled Material Models in MOOSE
A NEML2 nodal-force interface for high-rate solid mechanics
WCCM 2026
Author Name & Co-authors
Idaho National Laboratory

## Slide 2: Advanced reactors bring dynamic-loading questions
2 / 20
Transportable microreactors, pebble-bed cores, accident scenarios: components must be qualified under impact and other high-rate loads
These events are wave-dominated and fast. Stress waves traverse the part in microseconds, with severe, localized plasticity
Predictive fidelity requires modern constitutive models. Rate- and temperature-dependent, with evolving internal state
Simulating them means explicit time integration with a material-model evaluation at every quadrature point, every step
TIMESCALES OF AN IMPACT EVENT
event duration
~100 µs
wave transit through part
~1–10 µs
stable explicit step
~10 ns
⇒ steps to simulate
104–105
Many steps × expensive material updates: high-rate simulation is compute-hungry in a very particular way.

## Slide 3: Two mature ecosystems and a gap between them
3 / 20
MULTIPHYSICS FE FRAMEWORKS (MOOSE)
Boundary conditions, contact, parallel domain decomposition
Coupled-physics machinery, in-situ output, meshing, restart
But: materials evaluated point-by-point on CPU inside the element loop
MODERN MATERIAL LIBRARIES (NEML2)
Composable constitutive models with automatic differentiation
Batched tensor evaluation on GPU or CPU (libTorch backend)
But: no mesh, no boundary conditions, no solver. Not a simulation code
?
per-point calls,
per-step copies
This talk: an interface where NEML2 assembles the nodal internal forces itself, batched and device-resident, while MOOSE keeps doing everything else.

## Slide 4: Governing equations of explicit solid dynamics
4 / 20
balance of linear momentum on the reference domain
total-Lagrangian weak form. Every integral is on the reference configuration
discretize in space: semi-discrete momentum equation
internal force from the first Piola–Kirchhoff stress at each quadrature point
Reference-domain integrals: shape functions, weights, and dof maps never change during the run. All material physics enters through the stress P at the quadrature points.

## Slide 5: The material model I: finite-strain kinematics
5 / 20
multiplicative split: Fᵖ carries the crush, elastic strain stays small
trial state: plastic flow frozen at the old Fᵖ
radial return on the trial elastic strain, one scalar unknown
linearized exponential-map plastic update
pull-back to the reference configuration, giving the PK1 stress of the weak form

## Slide 6: The material model II: Johnson–Cook flow and adiabatic heating
6 / 20
flow stress: strain hardening × thermal softening; prior cold work ε₀ᵖ sets the temper
rate form (inverted Johnson–Cook): smooth viscoplastic overstress law
adiabatic Taylor–Quinney heating, integrated inside the model (β = 0.9)
OFHC COPPER (CuH04 SHOT)
E, ν
117 GPa, 0.34
ρ, cₚ
8960 kg/m³, 385 J/kg·K
β, m
0.9, 0.98
A
129 MPa
B
308 MPa
n
0.47
C
0.022
ε₀ᵖ
0.14 (H04 temper)
green = Bayesian-calibrated against the recovered specimen (later in this talk)
Internal state (εᵖ, Fᵖ, T) advances inside the model every step.

## Slide 7: Explicit time integration: ExplicitMixedOrder
7 / 20
Central difference, as implemented in our ExplicitMixedOrder MOOSE integrator
pointwise divide, no solver
variable-Δt midpoint velocity update
displacement update
No Newton iterations, no global linear solve, no Jacobian. Each step is one residual evaluation plus vector updates.
MIXED ORDER
Displacements: central difference
First-order fields (temperature): forward Euler on the rate
Both advance in the same update loop.
Developed for this work and upstreamed: part of MOOSE solid mechanics today.

## Slide 8: Stability sets the step; the material sets the cost
8 / 20
Conditional stability (CFL): the step must resolve the fastest stress wave
element length over elastic wave speed
Millimeter elements: Δt ≈ 10 ns ⇒ 104–105 steps for a 100 µs event
Each step needs no solve. The runtime is the residual, and the residual is the constitutive update at every quadrature point
Advanced models (rate/temperature-dependent plasticity, internal state) make each of those updates expensive
ANATOMY OF ONE EXPLICIT STEP
constitutive update dominant
force assembly + scatter
time advance, BCs, output
schematic; plasticity dominates the step cost
Explicit runtime ≈ steps × material-update cost.

## Slide 9: MOOSE: the multiphysics host
9 / 20
Open-source multiphysics FE framework (Idaho National Laboratory). We keep all of this for free
Boundary conditions
full BC library, incl. the penalty and pressure BCs used in this work
Contact
mortar and node-face algorithms, architecture-compatible with this interface
Parallel execution
MPI domain decomposition, scalable assembly and solves
Coupled physics
heat conduction, neutronics, porous flow, ... in one input file
Meshing & output
mesh generators, adaptivity, in-situ Exodus/CSV output
Ecosystem
NQA-1 quality assurance; large application family (BISON, Grizzly, ...)
Everything in a high-rate simulation that is not the material update already exists here, parallel and production-tested.

## Slide 10: NEML2: the material engine
10 / 20
New Engineering Material model Library v2 (ANL, open source). Constitutive models as composable tensor programs
A MODEL = SMALL OPERATORS, COMPOSED
elasticity
flow rule
hardening
rate
sensitivity
state
update
declared in an input file; exact derivatives by automatic differentiation
Batched: all quadrature points evaluated in one batched call
Device-portable: libTorch (PyTorch C++) backend runs the same model on CPU or GPU
NEML2 library benchmark: 42,500 s (NEML, CPU) → 68 s on one GPU
ONE CALL, ALL POINTS
σ = model(ε, state) over the whole batch
GPUs want exactly this shape of work: wide, uniform, no per-point branching
NEML2 evaluates material models as batched tensor programs. It has no mesh, boundary conditions, or assembly. MOOSE does.

## Slide 11: What we built: two pillars, one force path
11 / 20
1
ExplicitMixedOrder integrator
Explicit central-difference integrator with mixed-order multiphysics (2nd-order mechanics + 1st-order fields)
Lumped mass via matrix tag. Zero linear iterations per step
Variable step size (Abaqus-style midpoint velocity averaging)
Upstreamed to MOOSE solid_mechanics
2
NEML2 nodal-force interface
NEML2 computes internal nodal forces itself, not just stress, for the whole mesh in batched tensor ops
Constitutive state lives on the device and advances in place between steps
Plugs into the explicit solve as a residual contribution. MOOSE BCs, outputs, and MPI are unchanged
Foundation, unchanged: MOOSE boundary conditions · parallel domain decomposition · meshing & output · contact (architecture-compatible)
All of it is open source in the MOOSE framework and solid-mechanics module; the NEML2 force path is verified against conventional MOOSE on CPU and CUDA.

## Slide 12: One explicit step through the NEML2 force path
12 / 20
DEVICE (libTorch) · same code on CPU / CUDA
MOOSE
solution vector
(PETSc)
one upload / step
residual →
ExplicitMixed
Order
advance u
one download / step
NEML2FE
Interpolation
gather u, ∇u at
all quad points
NEML2Def
Gradient
F = I + ∂u/∂X
whole batch
NEML2Model
Executor
P = model(F, state)
one batched call
NEML2Stress
Divergence
Rᵉ = Σ ∇φ·P JxW
all elements at once
next explicit step (Δt ≈ 10 ns)
built once, cached on device: shape functions φ, ∇φ, DOF maps, weights JxW. Rebuilt only on mesh change
The interior force computation never touches an element loop: a short sequence of batched tensor ops.

## Slide 13: Constitutive state never leaves the device
13 / 20
CONVENTIONAL COUPLING · state round-trips through MOOSE every step
HOST
DEVICE
state in MOOSE material properties
age state: old ← current
batched stress + state update
state copied down and back up every step. Traffic scales with model complexity
THIS WORK · state advances in place on the device (manage_state_advance)
HOST
DEVICE
solution u
nodal forces F
state (Eᵖ, εᵖ, T, ...) advances in place
per step: one solution upload, one force download. Independent of model complexity
State stays where it is computed. Transfer volume does not grow with model complexity.

## Slide 14: The method, in one slide
14 / 20
1
Explicit runtime ≈ steps × material-update cost
CFL fixes the step count; the constitutive update is the only lever
2
ExplicitMixedOrder advances mechanics + first-order fields, no solver
lumped mass, zero linear iterations; upstreamed to MOOSE
3
NEML2 assembles the internal nodal forces on the device
batched over all elements; state advances in place; one upload + one download per step
4
MOOSE keeps BCs, parallelism, outputs unchanged
and the path is verified to match conventional MOOSE assembly (CPU and CUDA test suite)
Up next: the experiment · Taylor impact simulation · calibration against the scanned specimen

## Slide 15: The experiment
15 / 20
▶
high-speed video placeholder
impact and rebound of shot CuH04, high-speed camera
Specimen
OFHC copper slug, Ø 7.62 mm × 38.1 mm, H04 full-hard temper
Shot
235.9 m/s impact against a rigid anvil
Recovered geometry
laser-scanned to a 46k-triangle surface mesh
Role in this talk
the scan is the calibration and validation target

## Slide 16: Taylor anvil impact, end to end
16 / 20
OFHC copper slug at 235.9 m/s · calibrated multiplicative Johnson–Cook · reduced integration · Δt = 10 ns · 9,600+ explicit steps
cutaway views (near half removed). Plastic strain localizes at the impact foot. The gray plane is the rigid anvil
Same mesh, BCs, integrator. The temper is swapped by one NEML2 parameter: the prior cold work (initial plastic strain)
Full-hard 39% vs annealed 43% axial shortening

## Slide 17: The simulated impact
17 / 20
perspective view
side profile, the high-speed camera framing
Calibrated model, run to rebound at 96.9 µs. Color is effective plastic strain.

## Slide 18: Coupled thermo-mechanics: heating from plastic work
18 / 20
The run you just saw is coupled. Temperature is integrated inside the NEML2 model (adiabatic Taylor–Quinney heating, β = 0.9)
temperature rise above 300 K, cutaway views. Run to rebound at 96 µs with >99% of the impact kinetic energy dissipated
Feeds back into the flow stress
the hot foot softens (Johnson–Cook Θ = 1 − T*ᵐ) and flows more easily
Adiabatic by physics, not assumption
diffusion length √(αt) ≈ 0.1 mm ≪ element size over the ~100 µs run. No heat-conduction PDE needed
Three extra NEML2 model blocks
no new MOOSE modules, no new transfers. Temperature state lives on the device like everything else

## Slide 19: Bayesian calibration of the material parameters
19 / 20
Unknowns: θ = (A, B, n, C, ε₀ᵖ) plus a model-discrepancy scale σd. The forward model in the loop is the production simulation itself.
Priors
A, B lognormal, ×/÷ 2 at 90% around literature values. n ∈ [0.1, 0.5], C ∈ [0.01, 0.05], ε₀ᵖ ∈ [0.1, 0.5] uniform. Discrepancy half-normal (0.15 mm).
96-run Sobol design
one production simulation per point (~21 min each)
Gaussian-process emulator
PCA of the outer profile, one GP per mode. Cross-validated to 0.03 mm.
MCMC posterior
emcee over parameters and discrepancy. The posterior median is re-run through the true model.
posterior over parameters and discrepancy
Gaussian over ~40 profile stations, final length, and foot radius

## Slide 20: Validation: calibrated against a scanned specimen
20 / 20
Laser-scanned recovered specimen (OFHC copper, 235.9 m/s) → axis-corrected profile target → Bayesian calibration of the Johnson–Cook parameters
final deformed profile, production model at the calibrated posterior median
81 µm profile RMS
Bayesian posterior median
69 µm profile RMS
+ frictionless anvil